## Slide 1: Lab Session 6 Register File

## Slide 2: Register File Read hardware ( 32 registers)

## Slide 3: Register File write hardware

## Slide 4: Register file using LogiSim
Let size of the register = 4 bits
Number of Registers = 4
Steps involved
  Design a 2 to 4 Decoder - use analyse circuit and truth table method
  Design MUX ( 4 to 1 multibit ) – use the 4 to1 single bit MUX and expand it to multibit
  Drag 4 registers from Logisim toolkit and change their data bits to 4
  Drag four AND gates from Logi Sim Toolkit (gate size =narrow, number of input =2)
  Connect all the blocks
  Implement all circuits in the existing file ( expt 4)

## Slide 5: Decoder Design
Go to Project  Analyse circuit
Add S0 and S1 as input
D0,D1,D2 and D3 as output
Go to truth table
Change the output values as per the truth table of 2 to 4 decoder
Build the circuit

## Slide 6: Decoder

## Slide 7: Multibit MUX
Project  add circuit
Drag 4 blocks of 4 to 1 single bit MUX
Give four input variables with data bits =4 ( input A,B
Connect the inputs through splitters ( fan out = 4, bit width in =4)
Provide two select inputs S0 and S1 to all blocks
Take the final output through a splitter
Give proper labels to all input and output variables

## Slide 8: 4 to 1 MultiBit MUX

## Slide 9: Register File
Drag 4 register blocks from memory folder of Logisim toolkit
Set their data bits =4
Drag 4 AND gates from Gates folder
Drag 1 block of 2 to 4 Decoder
Connect output of AND gate to enable pin of each register
Drag clock input from wiring folder
Connect clock to clock pin of each register ( denoted as a triangle on the block)
Drag 2 units of multibit MUX
Complete the connections

## Slide 11: Combining ALU and Register file
Test and verify the register file
Remove the output variables ‘readport1’ and readport2 from the register file
Drag one block of 4 bit ALU
Connect the output of MUX 1 of the register file to 4 bit data input A
Connect the second output to data input B of ALU
Provide 4 bit constant input , Cin and three select inputs for ALU
Provide required output ports for ALU
Test and verify the total circuit